Ćw_1 – Przełączniki i diody LED, multipleksery, konwertery.

Zadanie 1 - przełączniki

library ieee; -- pokazanie katalogu z bibliotekami

use ieee.std_logic_1164.all;

-- Prosty moduł łączący przełączniki SW z diodami LEDR

-- nazwa jednostki projektowej po dyrektywie ENTITY taka jak pliku projektu

ENTITY zad_1 IS

PORT

(

SW : IN STD_LOGIC_VECTOR(9 DOWNTO 0); -- 10 przełączników

LEDR : OUT STD_LOGIC_VECTOR(9 DOWNTO 0) -- 10 diod LED

);

END zad_1;

ARCHITECTURE zachowanie OF zad_1 IS

BEGIN

LEDR <= SW;

END zachowanie;

Następnie:

- skompilować

- przypisać piny

- ponownie skompilować

Zadanie 2 - multiplekser

library ieee; -- pokazanie katalogu z bibliotekami

use ieee.std_logic_1164.all;

entity zad_2 is

port

(

x0,x1,x2,x3,x4,x5,x6,x7,y0,y1,y2,y3,y4,y5,y6,y7,s : in std_logic;

m0,m1,m2,m3,m4,m5,m6,m7 : out std_logic

);

end zad_2;

architecture inne of zad_2 is

begin

m0 <= (NOT (s) AND x0) OR (s AND y0);

m1 <= (NOT (s) AND x1) OR (s AND y1);

m2 <= (NOT (s) AND x2) OR (s AND y2);

m3 <= (NOT (s) AND x3) OR (s AND y3);

m4 <= (NOT (s) AND x4) OR (s AND y4);

m5 <= (NOT (s) AND x5) OR (s AND y5);

m6 <= (NOT (s) AND x6) OR (s AND y6);

m7 <= (NOT (s) AND x7) OR (s AND y7);

end inne;

Zadanie 3 - konwerter

library ieee;

use ieee.std_logic_1164.all;

entity zad_3 is

port

(

c,d : in std_logic_vector(2 downto 0);

hex1,hex2 : out std_logic_vector(6 downto 0)

);

end entity;

architecture litery of zad_3 is

begin

with c select

hex1 <=	"0001001" when "000",

"0000110" when "001",

"1000111" when "010",

"1000000" when "011",

"1111111" when others;

with d select -- kolejny segment

hex2 <=	"0001001" when "000",

"0000110" when "001",

"1000111" when "010",

"1000000" when "011",

"1111111" when others;

end litery; --komentarz do końca linii