Tester LT 8100 firmy Wavetek

| Call out | DH Front Panel | Description |
| --- | --- | --- |
| 1 | Graphical Display | Present menus, test results, graphs, action choices and option keys. |
| 2 | Option Keys | Select menu options displayed on screen. |
| 3 | Autotest Key | Perform a fast suite of tests. Test results are presented as pass/fail. Suites for established standards are preprogrammed in the tester. |
| 4 | Arrow Keys | Allow up, down, left, and right movement on the display. |
| 5 | Wiremap Key | Find shorts, opens and miswires such as split and reversed pairs. |
| 6 | Length Key | Initiate a Length test. |
| 7 | Enter Key | Select a highlighted option. Save changes. |
| 8 | Alphanumeric Keys | Enter numbers, letters or special characters. Select numbered menu options. |
| 9 | Escape Key | Abort and exit the current screen without making changes. |
| 10 | Cable Selection Key | Select a cable type. |
| 11 | Backlight Key | Toggle the screen backlight on/off. |
| 12 | On/Off Switch | Power the Display Handset on/off. |
| 13 | Low-Crosstalk Connector Port | Connect a test access cable. |
| 14 | Talkset Jack | Connect an Optional Talkset |
| 15 | DB-9 Serial Port | Printer and PC upload port. Also used to load software upgrades. |
| 16 | DC Input Jack | Connect an external power supply. |

Ready Screen

Ready Screen Indicators

| Indica tor | Function | Description |
| --- | --- | --- |
| 1 | Memory Usage | Display the total number of records stored. |
| 2 | Battery Meter AC Cable | Display remaining battery power level (from Empty to Full). Indicate when the unit is running off AC power. |

| 3 | Talk Set Indicator | Indicate when the Talk Set function is available. |
| --- | --- | --- |
| 4 | Screen Title | Display the Screen Title. |
| 5 | Time and Date | Display time and date information. |
| 6 | Setting | Display the cable type selected for testing. |
| 7 | Label | Display the current job name. |
| 8 | Label | Display the screen title for the highlighted function. |

Ready Screen Functions

| Icon | Function | Purpose |
| --- | --- | --- |
| 9 | Cable ID | Select the cable naming function. |
| 10 | Test Record | Select the stored test file manager. |
| 11 | Field Calibration | Select the field calibration screens. |
| 12 | Preferences | Select the instrument preferences screen. |
| 13 | Instrument Information | Select the instrument information screen. |
| 14 | Analyze | Select option to perform individual cable tests (real time). |
| 15 | Talk Set Select | Activate/deactivate the Talk set function |
| 16 | Help | Select the Information Screen. |

#### Soft Keys

Soft Key Descriptions

| Soft Key | Description |
| --- | --- |
|  | Okay or confirm an action. |
|  | Stop or cancel an action. |
|  | Print data. |
|  | Save data using Auto Increment naming convention. |
|  | Overwrite or rename data. |
|  | Run the selected test in continuous mode (real time). |
|  | Page-up for information. |
|  | Page-down for information. |
|  | Select/Deselect an item in a list box. Check boxes are on-off switches If a check box is turned on, the box will contain a check mark. |
|  | Select an action item. |
|  | Activate/Deactivate the Talk Set option. |
|  | Delete characters. |

RH Buttons, LED’s, and Connectors

| Callout | RH Front Panel | Description |
| --- | --- | --- |
| 1 | Pass LED | Successful test results |
| 2 | Fail LED | Unsuccessful test results |
| 3 | Testing LED | Test in progress |
| 4 | Talkset LED | Talkset is active |
| 5 | Tone LED | Toner is in operation |
| 6 | High Voltage LED | Excessive line voltage present (TELCO) |
| 7 | No Patch Cable LED | No patch cable connected |
| 8 | Battery Level LED’s | Remaining battery life |
| 9 | Tone switch | Press to activate/deactivate Toner |
| 10 | Low-Crosstalk Connector Port | A test access cable connector |
| 11 | DB-9 Serial Port | Use to interface to a PC |
| 12 | Talkset Jack | Connect an Optional Talkset |
| 13 | DC Input Jack | Connect an external power supply |

Analyze Single Test Mode Overview

- Wire Map – mapa połączeń

- Wire Length – długość toru transmisyjnego

- NEXT (Near-End Crosstalk) – przesłuch NEXT

- Attenuation – tłumienie

- Power Sum NEXT – przesłuch PS NEXT

- DC Resistance – stałoprądowa rezystancja pętli

- Return Loss – straty odbiciowe

- Delay and Skew – opóźnienie propagacji i rozrzut opóźnienia

- Impedance – impedancja falowa

- Power Sum ACR – różnica pomiędzy PS NEXT i tłumieniem

- Capacitance – pojemność elektryczna

- ACR – różnica pomiędzy NEXT i tłumieniem

- Headroom

- ELFEXT (Equal-Level Far-End Crosstalk) – przesłuch EL FEXT

- Power Sum ELFEXT (Power Sum Equal-Level Far-End Crosstalk) – przesłuch PS EL FEXT